## Slide 1: ROS

## Slide 2: Remember

## Slide 3: Workspace
my_project_ws
package_1 node_a node_b node_c package_2 node_d node_e

## Slide 4: Steps
Create workspace
  $ mkdir -p catkin_ws/src
  $ cd catkin_ws/
  $ catkin_make
Create Package
  $ cd src
  $ catkin_create_pkg my_package
  Put your python codes in my_package/scripts
  Add #!/usr/bin/env python to the first line of your code
  Modify my_package/CMakeLists.txt

## Slide 5: Steps
Add the following to the end of your CMakeLists.txt
catkin_install_python(PROGRAMS scripts/publisher.py scripts/subscriber.py DESTINATION ${CATKIN_PACKAGE_BIN_DESTINATION})
$ catkin_make in your catkin_ws directory
Add the $ source catkin_ws/devel/setup.bash to your ~/.bashrc
$ chmod -R +x my_package/scripts
Open a new terminal and run your nodes
  $ rosrun my_package publisher.py
  $ rosrun my_package subscriber.py

## Slide 6: Launch files
Run multiple nodes at once!

## Slide 7: Turtlebot
https://automaticaddison.com/how-to-launch-the-turtlebot3-simulation-with-ros/
Don’t forget to
  Put source devel/setup.bash of your workspace in the ~/.bashrc
  export TURTLEBOT3_MODEL=burger

## Slide 8: Turtlebot
Run the simulator
  $ roslaunch turtlebot3_gazebo turtlebot3_world.launch
Run gmapping slam
  $ roslaunch turtlebot3_slam turtlebot3_slam.launch slam_methods:=gmapping
  Don’t forget to sudo apt install ros-kinetic-slam-gmapping
Control the robot using keyboard
  roslaunch turtlebot3_teleop turtlebot3_teleop_key.launch

## Slide 9: Investigate
rosnode list
rostopic list
rostopic hz/echo/info cmd_vel (guess the output of info)
rostopic hz/echo/info imu (guess the output of info)
rostopic hz/echo/info scan (guess the output of info)

## Slide 10: Explore
RVIZ
Launch files

## Slide 11: Very useful resources
http://wiki.ros.org/ROS/Tutorials
Book: A Gentle Introduction to ROS
Robot navigation in simulation https://www.youtube.com/playlist?list=PLTEmcYHVE7dPWixFnzkd68jPjwGzxHjUG

## Slide 12: Very useful resources
SLAM Course https://www.youtube.com/playlist?list=PLgnQpQtFTOGQrZ4O5QzbIHgl3b1JHimN_